NEW Ford FIESTA ACTIVE Specifications

Performance and Economy

| Fiesta Active |  |  |  |  |
| --- | --- | --- | --- | --- |
|  |  |  | Fuel consumption l/100 km | Performance |
| Engine* | Power PS | CO2 g/km | Urban | Extra Urban | Combined | Max speed km/h (mph) | 0-100 km/h (0-62 mph) sec | 50-100 km/h (31-62 mph) sec* |
| 1.0 EcoBoost | 85 | 113 | 5.9 (47.9) | 4.4 (64.2) | 5.0 (56.5) | 170 (106) | 12.7 | 11.9 |
| 1.0 EcoBoost | 100 | 114 | 5.9 (47.9) | 4.4 (64.2) | 5.0 (56.5) | 181 (112) | 11.0 | 11.6 |
| 1.0 EcoBoost auto | 100 | 139 | 7.8 (36.2) | 5.2 (54.3) | 6.1 (46.3) | 177 (110) | 12.8 | N/A |
| 1.0 EcoBoost | 125 | 114 | 5.9 (47.9) | 4.4 (64.2) | 5.0 (56.5) | 191 (119) | 10.4 | 10.4 |
| 1.0 EcoBoost | 140 | 119 | 6.3 (44.8) | 4.6 (61.4) | 5.2 (54.3) | 200 (124) | 9.4 | 8.9 |
| 1.5 TDCi (without Auto Start-Stop) | 85 | 108 | 4.7 (60.1) | 3.9 (72.4) | 4.2 (67.3) | 170 (106) | 12.6 | 12.8 |
| 1.5 TDCi | 85 | 103 | 4.4 (64.2) | 3.7 (76.3) | 4.0 (70.6) | 170 (106) | 12.6 | 12.8 |
| 1.5 TDCi | 120 | 112 | 4.8 (58.9) | 4.1 (68.9) | 4.4 (64.2) | 190 (118) | 9.4 | 9.1 |

All engines feature Auto-Start-Stop unless indicated

* In 4th gear

WEIGHTS AND DIMENSIONS

Weights

| Fiesta Active (without openable panorama roof) |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  | Kerb weight (kg)# | Gross Vehicle Mass (kg) | Gross Train Mass (kg) | Max. Towable Mass (braked) (kg) | Max. Towable Mass (unbraked) (kg) | Nose weight (kg) | Roof load (kg) |
| 1.0 EcoBoost 85 PS | 1241 | 1685 | 2685 | 1000 | 620 | 65 | 50 |
| 1.0 EcoBoost 100 PS | 1241 | 1685 | 2685 | 1000 | 620 | 65 | 50 |
| 1.0 EcoBoost 100 PS Auto | 1284 | 1690 | 2690 | 1000 | 640 | 45 | 50 |
| 1.0 EcoBoost 125 PS | 1241 | 1685 | 2685 | 1000 | 620 | 65 | 50 |
| 1.0 EcoBoost 140 PS | 1241 | 1685 | 2685 | 1000 | 620 | 65 | 50 |
| 1.5 TDCi 85 PS No Stop Start | 1261 | 1690 | 2440 | 750 | 630 | 50 | 50 |
| 1.5 TDCi 85 PS | 1265 | 1690 | 2440 | 750 | 630 | 45 | 50 |
| 1.5 TDCi 120 PS | 1279 | 1710 | 2710 | 1000 | 635 | 50 | 50 |

# Represents the lightest kerbweight assuming driver at 75 kg, full fluid levels and 90 per cent fuel levels, subject to manufacturing tolerances and options, etc., fitted.

Towing limits quoted represent the maximum towing ability of the vehicle at its Gross Vehicle Mass to restart on a 12 per cent gradient at sea level. The performance and economy of all models will be reduced when used for towing.  Gross Train Mass includes trailer weight

Dimensions

| Dimensions (mm) | Active |
| --- | --- |
| Exterior |  |
| Overall length | 4068 |
| Overall width with/without/folded mirrors | 1941/1756/1783 |
| Overall height | 1498 |
| Wheelbase | 2493 |
| Front track | 1513 |
| Rear track | 1476 |
| Front overhang | 857 |
| Rear overhang | 718 |
| Min ground clearance (unloaded) | 152 |
| Min ground clearance (loaded) | 130 |
| Interior |  |
| Front headroom | 992 |
| Front max legroom | 1125 |
| Front shoulder room | 1347 |
| Rear headroom | 955 |
| Rear legroom | 835 |
| Rear shoulder room | 1301 |
| Luggage capacity (litres) |  |
| 5-seat mode, laden to package tray (with tyre repair kit) | 311 |
| 2-seat mode, laden to roof (with tyre repair kit) ‡ | 1093 |
| Fuel tank capacity (litres) |  |
| Petrol/Diesel | 42/40 |

‡ Measured in accordance with ISO 3832. Dimensions may vary dependent on the model and equipment fitted.

DRIVER ASSISTANCE TECHNOLOGIES

Adaptive Cruise Control

Adjustable Speed Limiter

Auto High Beam

Blind Spot Information System

Cross Traffic Alert

Forward Collision Warning

Rear Park Aid (sensors)

Rear parking camera

Hill Launch Assist

Lane Keeping Aid

Lane Keeping Alert

Pre-Collision Assist with Pedestrian Detection

Traffic Sign Recognition

SAFETY

Airbags: driver front, driver side, passenger front, passenger side, curtain x 2

Electronic Emergency Brake Assist

Electronic Stability Control

Front and rear outer seat load limiters and pre-tensioners

Driver’s seatbelt with locking tongue

ISOFIX child seat hard points

Passenger airbag deactivation with indicator

Rear seatbelt reminder

STEERING

| System | Rack and pinion with Electronic Power Assisted Steering (EPAS) |
| --- | --- |
| Ratio | 14.6:1 |
| Turning circle (m) | 10.3 kerb-to-kerb |

CHASSIS

| Front suspension | Independent suspension with MacPherson struts, L-shaped lower control arm, steering gear and hollow stabiliser bar mounted on subframe. Unique steering knuckle geometry. Hydraulic rebound stopper |
| --- | --- |
| Rear suspension | Twistbeam rear suspension with toe-correcting bush |

BRAKES

|  | Front | Rear |
| --- | --- | --- |
| Braking | Hydraulically operated dual-circuit system with diagonal distribution. Vented front discs. Rear drums. Rear discs for vehicles with powertrains with above 100 PS (excluding 100PS). Electronic four-channel anti-lock braking system (ABS) with electronic brake-force distribution (EBD), Electronic Stability System (ESP) and Emergency Brake Assist (EBA). Optional autonomous emergency braking (AEB) as part of Pre-Collision Assist with Pedestrian Detection |
| Disc/Drum dimensions (mm) | Ø262 x 23 | Ø 202.8 drum Ø252x12 disc (models above 100 PS) |
| Piston dimensions (mm) | Ø54 | Ø 20.64 drum Ø36 disc (above 100 PS) |

WHEELS & TYRES

| Alloy wheels |  |
| --- | --- |
| 17-inch x 7-inch | 205/45-R17 |

AERODYNAMICS

| Model (5dr) | Engine | Cd | A (m2) |
| --- | --- | --- | --- |
| Active | 1.0-litre Ecoboost | 0.328 | 2.16 |
| Active | 1.5-litre TDCi 85 PS | 0.325 | 2.16 |
| Active | 1.5-litre TDCi 120 PS | 0.349 | 2.16 |

PETROL ENGINES

|  |  | 1.0-litre EcoBoost (85, 100, 125, 140 PS) manual | 1.0-litre EcoBoost (100PS) automatic |
| --- | --- | --- | --- |
| Type |  | Inline three cylinder turbo petrol, Ti-VCT, transverse | Inline three cylinder turbo petrol, Ti-VCT, transverse |
| Displacement | cm3 | 998 | 998 |
| Bore | Mm | 71.9 | 71.9 |
| Stroke | Mm | 82.0 | 82.0 |
| Compression ratio |  | 85/100 PS 10.5:1, 125/140 PS 10.0:1 | 10.0:1 |
| Max power | PS (kW) | 85 (63) | 100 (74) | 125 (92) | 140 (103) | 100 (74) |
|  | at rpm | 4000-6000 | 4500-6500 | 6000 | 6000 | 4500-6500 |
| Max torque | Nm | 170 | 170 | 170 | 180 | 170 |
|  | at rpm | 1500-3500 | 1500-4000 | 1500-4500 | 1500-5000 | 1500-4000 |
| Valve gear |  | DOHC with 4 valves per cylinder, twin independent variable cam timing | DOHC with 4 valves per cylinder, twin independent variable cam timing |
| Cylinders |  | 3 in line | 3 in line |
| Cylinder head |  | Cast aluminium | Cast aluminium |
| Cylinder block |  | Cast iron | Cast iron |
| Camshaft drive |  | Low friction Belt-in-Oil with dynamic tensioner | Low friction Belt-in-Oil with dynamic tensioner |
| Crankshaft |  | Cast iron, 6 counterweights, 4 main bearings | Cast iron, 6 counterweights, 4 main bearings |
| Engine management |  | Bosch MED17 with CAN-Bus and individual cylinder knock control. FGEC Software | Bosch MED17 with CAN-Bus and individual cylinder knock control. FGEC Software |
| Fuel injection |  | High pressure direct fuel injection with 6 hole injectors | High pressure direct fuel injection with 6 hole injectors |
| Emission level |  | Euro Stage 6 | Euro Stage 6 |
| Turbocharger |  | Continental low inertia turbo | Continental low inertia turbo |
| Lubrication system |  | Electronically controlled variable displacement oil pump for improved fuel economy | Electronically controlled variable displacement oil pump for improved fuel economy |
| System capacity with filter | Litres | 4.6 | 4.6 |
| Cooling system |  | Split cooling system with 2 thermostats | Split cooling system with 2 thermostats |
| System capacity incl heater | Litres | 5.8 | 5.8 |
| Transmission |  | 6-speed manual | 6-speed torque converter automatic |
| Gear ratios |  |  |  |  |  |
|  |  | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 3.941 | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 3.941 | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 3.941 | 6th 0.634 5th 0.757 4th 0.943 3rd 1.276 2nd 1.958 1st 3.417 R 3.833 FDR 4.353 | N/A |

DIESEL ENGINES

|  |  | 1.5-litre TDCi (85 PS) | 1.5-litre TDCi (120 PS) |
| --- | --- | --- | --- |
| Type |  | Inline four cylinder turbo diesel, transverse | Inline four cylinder turbo diesel, transverse |
| Displacement | cm3 | 1499 | 1499 |
| Bore | Mm | 73.5 | 73.5 |
| Stroke | Mm | 88.3 | 88.3 |
| Compression ratio |  | 16.0:1 | 16.0:1 |
| Max power | PS (kW) | 85 (63) | 120 (88) |
|  | at rpm | 3750 | 3600 |
| Max torque | Nm | 215 | 270 |
|  | at rpm | 1750-2500 | 1750-2500 |
| Valve gear |  | SOHC with 2 valves per cylinder | SOHC with 2 valves per cylinder |
| Cylinders |  | 4 in line | 4 in line |
| Cylinder head |  | Cast aluminium | Cast aluminium |
| Cylinder block |  | Cast Aluminium with cast iron cylinder liners | Cast Aluminium with cast iron cylinder liners |
| Camshaft drive |  | Timing belt | Timing belt |
| Crankshaft |  | Steel forging | Steel forging |
| Engine management |  | Bosch FDEC | Bosch FDEC |
| Fuel injection |  | High pressure common rail diesel injection system with 8 hole nano sac nozzle injectors | High pressure common rail diesel injection system with 8 hole nano sac nozzle injectors |
| Emission level |  | Euro Stage 6 | Euro Stage 6 |
| Turbocharger |  | Fixed geometry turbo | Variable geometry turbo |
| Lubrication system |  | Variable displacement oil pump direct driven from the crankshaft belt for improved fuel economy | Variable displacement oil pump direct driven from the crankshaft belt for improved fuel economy |
| System capacity with filter | litres | 3.8 | 3.8 |
| Cooling system |  | External single tube with integral thermostat | External single tube with integral thermostat |
| System capacity | litres | 6.5 | 6.5 |
| Transmission |  | 6-speed manual | 6-speed manual |
| Gear ratios |  |  |  |
|  |  | 6th 0.568 5th 0.683 4th 0.865 3rd 1.172 2nd 1.880 1st 3.417 Reverse 3.833 FDR 3.550 | 6th 0.622 5th 0.738 4th 0.919 3rd 1.258 2nd 2.048 1st 3.727 Reverse 3.818 FDR 3.350 |

# # #

Note: The data information in this press release reflects preliminary specifications and was correct at the time of going to print. However, Ford policy is one of continuous product improvement. The right is reserved to change these details at any time.

Note: The declared Fuel/Energy Consumptions, CO2 emissions and electric range are measured according to the technical requirements and specifications of the European Regulations (EC) 715/2007 and (EC) 692/2008 as last amended. Fuel consumption and CO2 emissions are specified for a vehicle variant and not for a single car. The applied standard test procedure enables comparison between different vehicle types and different manufacturers. In addition to the fuel-efficiency of a car, driving behaviour as well as other non-technical factors play a role in determining a car's fuel/energy consumption, CO2 emissions and electric range. CO2 is the main greenhouse gas responsible for global warming.

From 1 September 2017, certain new vehicles will be type-approved using the World Harmonised Light Vehicle Test Procedure (WLTP) according (EU) 2017/1151 as last amended, which is a new, more realistic test procedure for measuring fuel consumption and CO2 emissions. From 1 September 2018 the WLTP will fully replace the New European Drive Cycle (NEDC), which is the current test procedure. During NEDC Phase-out, WLTP fuel consumption and CO2 emissions are being correlated back to NEDC. There will be some variance to the previous fuel economy and emissions as some elements of the tests have altered i.e., the same car might have different fuel consumption and CO2 emissions.

# About Ford Motor Company

Ford Motor Company is a global company based in Dearborn, Michigan. The company designs, manufactures, markets and services a full line of Ford cars, trucks, SUVs, electrified vehicles and Lincoln luxury vehicles, provides financial services through Ford Motor Credit Company and is pursuing leadership positions in electrification, autonomous vehicles and mobility solutions. Ford employs approximately 202,000 people worldwide. For more information regarding Ford, its products and Ford Motor Credit Company, please visit www.corporate.ford.com.

Ford of Europe is responsible for producing, selling and servicing Ford brand vehicles in 50 individual markets and employs approximately 54,000 employees at its wholly owned facilities and approximately 69,000 people when joint ventures and unconsolidated businesses are included. In addition to Ford Motor Credit Company, Ford Europe operations include Ford Customer Service Division and 24 manufacturing facilities (16 wholly owned or consolidated joint venture facilities and eight unconsolidated joint venture facilities). The first Ford cars were shipped to Europe in 1903 – the same year Ford Motor Company was founded. European production started in 1911.

|  | Contact: Finn Thomasen Ford of Europe +44 (0) 1268 401 908 fthomas3@ford.com |
| --- | --- |